## Slide 1
Processing High-Scale Messaging using Service Bus, Event Hub & IoT Hub

## Slide 2: Agenda
Azure IoT reference architecture
Pushing and reading messages
  Event Hub
  IoT Hub
Scaling patterns
Command Control Introduction
Notes: This session with introduce the IoT architecture, show samples on how to push messages to an event hub, an Iot hub. Show examples on how to read messages and introduce the concept of command and control.
We will also discuss scaling options and patterns for understanding how to architect an IoT solution.

## Slide 3: Azure IoT Reference Architecture
Gateway
IP capable devices
Existing IoT devices
Low power devices
Agent
Agent
Agent
Solution Logic & UI
Provisioning API
Device Registry Store
Stream Event Processing
Analytics & Machine Learning
Device State Store
Device and Event Processing
Cloud Gateway
Presentation and Business Process Integration
Data Transport
Devices and Data Sources
Storage
Notes: Displayed is the IoT reference architecture. It depicts the typical architectural components of most IoT solutions.
Highlight:
Some devices are native “internet talking devices”
Other devices may use different protocols
Some devices may require a protocol translation or may not be internet enabled
Major components of an IoT solution are the provisioning and management of the devices, storage of telemetry data and analytics

## Slide 4: Azure IoT Suite Implementation
Gateway
IP capable devices
Existing IoT devices
Low power devices
Agent
Agent
Agent
Solution Logic & UI
Provisioning API
Device Registry Store
Stream Event Processor
Analytics & Machine Learning
Device State Store
Device and Event Processing
Cloud Gateway
Presentation and Business Process Integration
Data Transport
Devices and Data Sources
Storage
Notes: With the Azure IoT suite, Azure provides some of the major infrastructure required to quickly get running with IoT solutions.
With every architecture however, there different points of elasticity that are required to build a scalable, available system.
These points are highlighted
<<click>>
How we injest data at scale
How we process the data at scale
How we manage remote monitoring and updates of the devices
These are all scale points we need to consider for an IoT solution. We will dive into these areas during this talk.

## Slide 5: Microsoft Azure IoT services portfolio
Devices | Device Connectivity | Storage | Analytics | Presentation & Action
` | Event Hub | SQL Database | Machine Learning | App Service
 | IoT Hub | Table/Blob Storage | Stream Analytics | Power BI
 | Service Bus | DocumentDB | HDInsight | Notification Hubs
 | External Data Sources | 3rd party Databases | Data Factory | Mobile Services
 |  |  | Data Lake | BizTalk Services
{ }

## Slide 6: Pushing and reading messages

## Slide 7: Azure Service Bus
Azure Service Bus
Relay
Queue
Topic
Notification Hub
NAT and Firewall Traversal Service Request/Response Services Unbuffered with TCP Throttling
Transactional Cloud AMQP/HTTP Broker High-Scale, High-Reliability Messaging Sessions, Scheduled Delivery, etc.
Transactional Message Distribution
Up to 2000 subscriptions per Topic
Up to 2K/100K filter rules per subscription
High-scale notification distribution
Most mobile push notification services
Millions of notification targets
… this session …
Event Hub
IoT Hub

## Slide 8: Azure Service Bus
Architecture pattern and middleware designed to make business processes more loosely-coupled and have better interconnectivity between other business processes
Abstracting direct connections to other processes
Messaging
Contains
  Queues / Topics
  Relay
  Notification Hub
  Event Hub

## Slide 9: Azure Event Hubs
Event Producers
Azure Event Hub
> 1M Producers > 1GB/sec Aggregate Throughput
Up to 32 partitions via portal, more on request
Partitions
Direct
PartitionKey
Hash
Throughput Units:
1 ≤ TUs ≤ Partition Count
TU: 1 MB/s writes, 2 MB/s reads
Consumer Group(s)
Receivers
AMQP 1.0
Credit-based flow control
Client-side cursors
Offset by Id or Timestamp
Event Processor Host
IEventProcessor

## Slide 10: Partitions
Segmentation of the event stream for scale-out
  Parallelism for consumers pulling events for processing
  Parallelism for producers submitting events
Default 16, minimum 8, self-service maximum 32
  Azure Support can enable up to 1024 (or more under special conditions)
  Maximum 10 Event Hubs per namespace
Sender usage of partitions
  Direct targeting with partition-id allowing for sender controlled segmentation
  Automatic hash-based distribution by PartitionKey or Publisher Identity
  Automatic random distribution

## Slide 11: Throughput Units
Throughput Unit (TU): Quota and Billing Concept
  Write: Lesser of 1MByte/sec or 1000 message operations/sec (incl. management)
  Read: 2MByte/sec
  Included retention: 84GByte/day (24h at full ingress rate)
    Retention can be expanded w/ self-service up to 7 days, via Azure support up to 30 days
    Local-redundant Azure storage pricing for overages applies
Number of Partitions ≥ Throughput Units
  At most one throughput unit per partition, minimum is one
  10 partitions have 10 TU = 10 MByte/sec throughput ceiling
TUs are applied and enforced at the namespace level, i.e. across Event Hubs
  Maximum of 20 TUs per account in self-service.
  Further w/ commitments through Azure support (blocks of 20 up to 100, blocks of 100)
Billing
  TUs are billed by the hour (!) they are applied to a namespace

## Slide 12: Publishers
Very many publishers
  Short-lived, low throughput: HTTPS
  Long-lived, high throughput: AMQP
    Long lived AMQP connections are billable, HTTPS requests are not; AMQP connection allowance included in tier
Publish to …
  PartitionId
    Direct
  PartitionKey
    PartitionKey selecting PartitionId
  Publisher Policy (<eh>/publishers/<name>)
    <name> overriding PartitionKey
Event Producers
Direct
PartitionKey
Hash
Partitions

## Slide 13: Consumer Groups
Views on the Event Stream
  Conceptually similar to Topic subscriptions in that they are a ‘view’ on the event stream
  Organizational anchor for checkpointing (you)
  Anchor for creating per-partition receivers
  Default consumer group always present
  Can create up to 20 named consumer groups
“Receivers read through a consumer group”
Consumer Group(s)

## Slide 14: Consumers
Receive from partitions via consumer groups
  Using .NET API or using generic AMQP 1.0 client (e.g. Apache Proton-C/J)
Cursors (offsets) solely maintained by clients; not like Queue/Topic
  Maximum flexibility for consumption
  Can act as raw event history store for retention duration
    Not an archive, but raw data value often deteriorates quickly
  Can synchronize across streams by timestamp
  Checkpoints must be maintained by clients
Direct support for external leader election models with epochs
Partition
Event Log
ID, Time, [Data]
ID, Time, [Data]
ID, Time, [Data]
ID, Time, [Data]
ID, Time, [Data]
Time
ID

## Slide 15
Sending events to event hub

## Slide 16: Scaling patterns

## Slide 17: Intermediaries and Brokers
Intermediary
S
R
Broker
S
R
Query
Filter
Pull
Route
Intermediaries route messages ‘straight through’ with feedback path and network backpressure into sender
AuthN/Z
AuthN/Z
Brokers hold messages for retrieval and querying
Backpressure Feedback

## Slide 18: Push vs. Pull
Intermediary
S
R
Broker
S
R
‘Push’ is a sender initiated activity that results in delivery of a message to a receiver without the receiver explicitly asking for one or a particular message.
‘Pull’ is a receiver initiated activity that delivers stored messages to the receiver in a context that the receiver controls. The context is decoupled from the ‘Push’ style send operation

## Slide 19: Ways to Pull
Receive and Delete
  Fastest. Message lost if receiver crashes or transmission fails.
Peek Lock
  Message is locked when retrieved. Reappears on broker when not deleted within lock timeout.
Transactional
  Local model
Broker
R
Receive and Delete
Broker
R
2. Delete/Unlock
Broker
R
Receive
1. Peek/Lock
Tx

## Slide 20: Competing Consumer
Load Balancing
  Multiple receivers compete for messages on the same queue (or subscription). Provides automatic load balancing of work to receivers volunteering for jobs.
  Observing the queue length allows to determine whether more receivers are required.
S
R
Queue
R
R

## Slide 21: Fan-In
Concentrator
  Fan information into a single queue from a range of data sources
Multi-Stage Aggregration / Rollup
  Fan into a set of queues, perform aggregation/roll-up/reduction and fan further.
S
R
Queue
S
S

## Slide 22: Taps and Fan-Out
Message Distribution
  Each receiver gets its own copy of each message. Subscriptions are independent. Allows for many independent ‘taps’ into a message stream. Subscriber can filter down by interest.
Constrained Message Distribution (Partitioning)
  Receiver get mutually exclusive slices of the message stream by creating appropriate filter expressions.
S
R
Topic
Sub
Sub
Sub
R
R

## Slide 23: Filtering
Up to 2000 rules per subscription
Each matched rule yields a message copy
SQL’92 expressions over message properties
S
R
Topic
Sub
Sub
Sub
R
R
Name LIKE ‘V%’

## Slide 24: Partitioning
Rule conditions form mutually exclusive ranges
Allows partitioning-aware message distribution
No need for sender to be aware of partitioning
S
R
Topic
Sub
Sub
Sub
R
R
PartId > 272 AND PartId <= 567
PartId > 0 AND PartId <= 272
PartId > 567 AND PartId <= 791

## Slide 25
Message reading with IEventProcessor

## Slide 26: Event Processor Host
NuGet package separate from SDK
Implements scale-out event processing over minimal dependencies on Azure
  Leader election through blob leases and blob lease breaking (stealing)
  Checkpointing in Azure Storage Blobs
  IEventProcessor supplied by user application
Alternatives
  Leader election via and checkpointing in ZooKeeper or DHTs
Coming very soon
  Storm Spout for Java using ZK

## Slide 27: Leases, IEventProcessor, ICheckpointManager
.NET API abstraction (considering for other SDKs)
Lease
  Partition lease abstraction for failover and scale inflate/deflate management
  Base class, represents externally acquired lease on leadership for the partition
ICheckpointManager
    Checkpoint storage abstraction for storing client offset in scale-out fabric
  Stores checkpoints (offsets for consumed events) in externally supplied store
IEventProcessor
  Event processor to handle batches of messages
  OpenAsync/ProcessEventsAsync/CloseAsync
  Registered on Consumer Group Client

## Slide 28
Reading messages at scale

## Slide 29: Pushing and reading messages (IoT Hub)

## Slide 30: Sample scenario-Tire sensors
Simulated car tires
  Emits telemetry as events happen
  Random pressure and speed
  Flat tires
Provision device
  Device registry to query devices and track provisioning
  Device identity and key stored in IoT hub
Device emits telemetry
  Event processor reads and acts
Cloud gateway pushes messages
IoT Hub
Device ID
C2D queue
endpoint
D2C send endpoint
Device …
Device …
Device …
D2C receive endpoint
C2D send endpoint
IoT Hub management
Event Processor
Device registry
Portal
Notes: The sample scenario used in the demo is tires and cars.
Each car has 4 tires installed and each tire will maintain information about pressure, diameter, miles, etc.
When each car is created, it will “self-register” with the IoT hub.
They will emit telemetry as the car is “moving’ to the IoT hub.

## Slide 31: Why IoT Hub?
Provides common infrastructure for:
  Device to cloud
  Cloud to device
  Gateways
Scales to millions of devices
  Per device identity, authentication and security
Notes: 200 units = 100k connected devices and many messages

## Slide 32: Azure IoT Hub
Designed for IoT
  Connect millions of devices
Service assisted communications
  Devices are not servers
  Use IoT Hub to enable secure bi-directional comms
Cloud-scale messaging
  Device-to-cloud and Cloud-to-device
  Durable messages (at least once semantics)
Cloud-facing feedback
  Delivery receipts, expired messages
  Device communication errors
Per-device authentication
  Individual device identities and credentials
Connection multiplexing
  Single device-cloud connection for all communications (C2D, D2C)
Multi-protocol
  Natively supports AMQP, HTTP
  Designed for extensibility to custom protocols
Multi-platform
  Device SDKs available for multiple platforms (e.g. RTOS, Linux, Windows)
  Multi-platform Service SDK.
Notes: Azure IoT Hub is a scalable, multi-tenant cloud platform (IoT PaaS) that includes an IoT device registry, data storage, and security. It also provides a service interface to support IoT application development. Learn how Azure IoT Suite helps you securely connect millions of Linux, iOS, Android, Windows, and real-time operating system (RTOS) devices to reliably send telemetry and receive commands from your application back-end in the cloud.

## Slide 33
IoT Hub Overview

## Slide 34: IoT Hub Creation Blades
Pricing is based on #of devices and hub units (messages)
Partitions are for event hub processing and ingest
Notes: Can I change it later? Yes from free to paid or from S1 to S2. No path for Standard to free

## Slide 35: Device-to-cloud messages
Interface
  AMQP and HTTPS device-side endpoint
  AMQP service-side endpoint
  Device and service SDKs
Compatible with Event Hubs
  Partitioned receiver, client check-pointing
  Integrations with Azure Stream Analytics, Storm, …
  100% compatible with Event Hubs receivers
IoT Hub services for D2C
  Millions of simultaneously connected devices
  Per-device authentication
  Connection-multiplexing:
  C2D and D2C traffic
  Across multiple devices for gateway scenarios
IoT Hub
Device id
C2D queue
endpoint
D2C send endpoint
Device …
Device …
Device …
D2C receive endpoint
C2D send endpoint
IoT Hub management

## Slide 36: Cloud-to-device messages
Interface
  AMQP and HTTPS device-side endpoint
  AMQP service-side endpoint
At-least-once semantics
  Durable messages
  Device acknowledges receipt (Send - Receive - Abandon OR Complete)
TTL and receipts
  Per-message TTL
  Per-message positive and negative receipts
Command lifecycle pattern
  Use correlated D2C for responses
  Use feedback information to retry
  Store command state in command registry
IoT Hub
Device id
C2D queue
endpoint
D2C send endpoint
Device …
Device …
Device …
D2C receive endpoint
C2D send endpoint
IoT Hub management
Msg feedback and monitoring endpoint

## Slide 37
Command Control Introduction

## Slide 40: IoT Hub endpoints
Event processing
(hot and cold path)
Device provisioning and management
Your IoT Hub
Device ID
C2D queue
endpoint
D2C send endpoint
Device …
Device …
Device …
D2C receive endpoint
C2D send endpoint
Msg feedback and monitoring endpoint
Device identity management
IoT Hub management
Device
Device business logic,
connectivity monitoring
Field GW/
Cloud GW
Notes: IoT Hub exposes a set of conceptual endpoints to access its functionalities.
There are two endpoints for each device: one to send D2C msgs, one to receive C2D msgs.
Devices can connect two both endpoints over the same connection.
FGW and CGW are able to represent multiple devices by simultaneously connecting to D2C and C2D endpoints for many devices at the same time.
On the app back-end side, the D2C receive endpoint is used by the event processing pipeline (ASA, Storm, custom, …), and by the device runtime logic component, which handles requests and command responses that come from devices.
The device runtime logic component also uses the C2D send endpoint to send notifications and commands to devices.
It also uses the msg feedback and monitoring endpoint. This is critical for IoT solutions where devices are reachable only through IoT Hub. In these very common scenarios, any problem on the connectivity between device and IoT Hub cannot just be reported as errors back to the device, but also to the app back-end in the form of events on this feedback endpoint. This makes possible the kind of monitoring that is required to achieve high operability of an IoT solution.
In addition to these runtime endpoint, IoT Hub also has a device identity mgmt endpoint that is used by your solution’s device provisioning and mgmt component.
Finally, an IoT Hub Manage endpoint is used to set security, functional, performance parameters.

## Slide 41: Connect Your Devices
Field gateway
Cloud protocol
gateway
IP-capable
PAN-devices
Event processing and insight
(e.g. hot and cold paths)
Device business logic,
Connectivity monitoring
Application
device provisioning and management
cloud
field
Event Hub

## Slide 42: Azure IoT Reference Architecture
Solution Portal
Provisioning API
Device Registry Store
Stream Event Processor
Analytics/ Machine Learning
Data Visualization & Presentation
Device State Store
Gateway
Storage
IP capable devices
Existing IoT devices
Low power devices
Presentation
Device and Event Processing
Data Transport
Devices and Data Sources
Azure IoT Hub
Agent
Agent
Agent

## Slide 43: Azure IoT Suite SDKs
Device-facing
  For devices and field gateway
Platforms
  RTOS (FreeRTOS)
  Linux (Ubuntu, Debian, Fedora, Raspbian, Angstrom)
  Windows 7/8/10
  ARM mbed
  Android
  iOS
  …
Languages
  C, Java, C#, Javascript
Service-facing
  For back-ends and cloud gateway
Languages
  .NET C#
  Java
  Node

## Slide 44: Queueing
Sender sends message to the queue, then receiver can pull off the queue
First In First Out (FIFO) message delivery
One-Way message
To imitate, Request/Reply pattern, a return queue needs to be created the sender will then for the responses

## Slide 45: Topics
Senders send messages to the SB that are then distributed to multiple subscribers.
Each subscriber has their own independent queue
TIP: Remember to allocate the right amount of space utilized for your queues or messages will bounce off SB.

## Slide 46: Relay
Exposes an endpoint for clients outside the network to gain access to internal systems

## Slide 47: When use Which?
Message Correlation (Queues)
  High throughput needs; work usually completes in minimal time
  It’s ok for the replying party to directly know of the reply destination
Subscription Correlation (Topics)
  Decoupling of replying party and destination
  Longer lived jobs that may require moving handling between subscriptions by ways of moving rules
Session Correlation
  Reliable multiplexed duplex communication

## Slide 48: Pricing
Basic: Up to 100 connections, no extension Standard: 1000 connections incl. | Price (US Dollars) | 
Throughput Unit Hour (Basic) | 0.015 | TU per hour
Throughput Unit Hour (Standard) | 0.03 | TU per hour
Ingress Events | 0.028 | per 1,000,000 events
Cost Brokered Connections (1k-100k) | 0.00004 | connection/hour
Cost Brokered Connections (100k-500k) | 0.00003 | connection/hour
Cost Brokered Connections (500k+) | 0.00002 | connection/hour
Storage Overage >TUs*84GB |  | local-redundant Azure storage charge-through